Routers :
A router helps you connect multiple devices to the Internet, and connect the devices to each other. Also, we can use routers to create local networks of devices.
Types of routers
### Wired routers
Wired routers usually connect directly to modems or wide-area networks (WANs) via network cables. They typically come with a port that connects to modems to communicate with the Internet.
### Wireless routers
Routers can also connect wirelessly to devices that support the same wireless standards. Wireless routers can receive information from and send information to the Internet.

### IP Routing
It is the procedure of transmitting the packets from the end device of one network to remote end device of some other network. This is accomplished by Routers.
Routers inspect the destination end IP address and next-hop address and according to results will forward the data packet to the destination.
Routing tables are used to find out the next hop addresses and destination addresses.

Default Gateway: A default gateway is nothing but a router itself. It is deployed in the network where an end device host doesn’t have next-hop route entry of some explicit destination network and don’t able to make out the way to arrive at that network.
Therefore the host devices are configured in such a way so that the data packets which are directed towards remote network will be destined firstly to the default gateway.
Then the default gateway will provide the route towards the destination network to the source end host device.

## Routing Table
The routers have the internal memory called as RAM. The all the information a routing table gathers will be stored in RAM of routers. A routing table identifies the path for a packet by learning the IP address and other related information from the table and forwards the packet to the desired destination or network.

The following are the entities contained in a routing table:
1. IP addresses and Subnet mask of the destination host and the network
2. IP addresses of all those routers which are required to reach the destination network.
3. Extrovert interface information

There are three various procedures for populating a routing table:
Directly connected subnets
Static routing
Dynamic routing

Connected Routes: In the ideal mode, all the interfaces of the routers will remain in ‘down’ state. So the interfaces on which user going to implement any configuration, firstly change the state from ‘down’ to ‘up’. Next step of configuration will be assigning the IP addresses to all interfaces.
Now the router will be smart enough to route the data packets to a destination network via directly connected active interfaces. The subnets are also added in the routing table.

Static Routing: By using static routing, a router can gather the route to the far end network that is not physically or straightly connected to one of its interfaces.
Routing is done manually be running a particular command which is globally used.

Dynamic Routing: This type of routing works with at least one type of routing protocol is facilitated with it. A routing protocol is practiced by routers so that they can share the routing information among them. By this process, each of the routers in the network can learn that information and will deploy it in building up their own routing tables.
Routing protocol works in such a way so that if a link goes down on which it was routing data, it dynamically change their path for routing packet which in turn makes them fault-resistant.
Dynamic routing also doesn’t need any manual configuration which saves the time and administration load.
We only need to define the routes and their corresponding subnets which router will be using and the rest is taken care by routing protocols.

### Types of Routing Protocols
There are two kinds of routing protocols:
1. Distance vector
2. Link state
Both above types of routing protocols are interior routing protocols (IGP) which denotes that they used to trade routing data inside one self-governing network system. While Border gateway protocol (BGP) is a type of exterior routing protocol (EGP) which denotes that it is used to trade routing data between two dissimilar network systems on the internet.

#### Distance vector Protocol

RIP (Routing Information protocol): RIP is a kind of Distance vector protocol. As per the name, distance vector routing protocol employ distance to obtain the best-suited path to reach the remote network. The distance is basically the count of routers exist in-between while approaching remote network. RIP has two versions but version 2 is most popularly used everywhere.
Version 2 has the ability to present subnet masks and practices multicast to send routing updates. Hop count is practiced as a metric and it has the administrative count of 120.
RIP version 2 launch the routing tables in every interval of 30 seconds thus lots of bandwidth is utilized in this process. It utilizes the multicast address 224.0.0.9 to launch routing information.

EIGRP (Enhanced interior gateway routing protocol): It is a progressive type of distance vector protocol.
The various types of routing aspects it backs are:
Classless routing and VLSM
Load balancing
Incremental updates
Route summarization
The routers which use EIGRP as a routing protocol practices the multicast address 224.0.0.10. EIGRP routers maintain three kinds of routing tables which has all the necessary information.
The administrative distance of EIGRP is 90 and it determines the metric by using bandwidth and delay.
#### Link State Protocol

The objective of link state protocol is also similar to that of distance vector protocol, to locate a best-suited path to a destination but deploy distinctive techniques to perform it.
Link state protocol doesn’t launch the overall routing table, in its place, it launches the information regarding the network topology as a result of which all the routers using link state protocol should have the similar network topology statistics.

These are difficult to configure and require much memory storage and CPU memory than distance vector protocol.

This works faster than that of distance vector protocols. They also maintain the routing table of three types and perform the shortest path first algorithm to find out the best path.

OSPF is a kind of link state protocol.
#### BGP :
Border Gateway Protocol (BGP) is the postal service of the Internet.
when someone submits data via the Internet, BGP is responsible for looking at all of the available paths that data could travel and picking the best route, which usually means hopping between autonomous systems.
BGP is the protocol that makes the Internet work by enabling data routing.

What is ASN?

Autonomous System Number (ASN) is a globally unique identifier that defines a group of one or more IP prefixes run by one or more network operators that maintain a single, clearly-defined routing policy. These groups of IP prefixes are known as autonomous systems.

OSPF (open shortest path first):
It is a classless routing protocol and backs VLSM (Variable Length Subnet Mask), incremental updates, manual route summarization and equal cost load balancing.
Only interface cost is used as a metric parameter in OSPF. The administrative distance number is set to 110. Multicast IP deployed for routing updates are 224.0.0.5 and 224.0.0.6.
The link between neighboring routers using OSPF protocol is firstly set up before sharing the routing updates. As it is a link state protocol so routers don’t float the entire routing table but only share the statistics regarding network topology.
Then each router performs SFP algorithm to determine the superlative path and includes it to the routing table. By using this process the possibility of routing loop error is least.
OSPF routers send the hello packets on multicast IP 224.0.0.5 to set up the link with neighbors. Then when the link is established then it starts floating routing updates to neighbors.
An OSPF router sends hello packets in every 10 seconds on the network. If it doesn’t receive the return hello packet from a neighbor in 40 seconds then it will proclaim that neighbor as down. Routers to become neighbors should have some fields as common as subnet ID, area id, hello and dead interval timers, authentication, and MTU.
OSPF has the process of each message authentication. This is used to avoid routers to transmit false routing information. The false information can lead to denial of service attack.
There are two methods of authentication, MD5, and clear text authentication. MD5 is most commonly used. It supports manual summarization process of routes while floating in routing tables.

IS – IS :
IS-IS is an IGP, link-state routing protocol, similar to OSPF. It forms neighbor adjacencies, has areas, exchanges link-state packets, builds a link-state database and runs the Dijkstra SPF algorithm to find the best path to each destination, which is installed in the routing table.

Unlike OSPF which was developed by the IETF (Internet Engineering Task Force), IS-IS was originally developed by DEC for CLNS, not IP and this is why it’s called IS-IS (Intermediate System – Intermediate System).
Later, IS-IS was adapted so that it could also route IP and is then called integrated IS-IS.

ssh -oKexAlgorithms=+diffie-hellman-group-exchange-sha1 -c aes128-cbc readonly@